## Slide 1: RVC
Robot Vacuum Cleaner

## Slide 2: RVC system
System point of view
As if we were a company producing the RVC system
Roomba, Dyson, Ariete, Moulinex, ..

## Slide 3: Req document
Stakeholders
Context diagram + interfaces
FR + NFR
UCD + UC + scenarios
Glossary
System design
Deployment diagram

## Slide 4: Stakeholders
End users (customers who will use the RVC system)
Component producers
Retailers (mediaworld ..)
Competitors
Std for power supply
Environment (houses or offices or industrial?)
Inside company
  Marketing office
  Design office
  Software office
  Engineering office

## Slide 5: Context diagram
Actor: end user (active)
Actor: power supply
Actor: maintenance server (passive)
Actor: obstacle, gap (passive)
interfaces
Actor | Log interface | Physical interface
End user | Start stop , .. | 3 buttons
Power supply |  | Plug schuko 3 poles, 220v
Maintenance server of producer company | Look for update, install update | Wifi connection
Obstacle, gap | Recognize obstacle or gap | IR used by sensor

## Slide 6: Functional requirement (system level)
Clean floors of house in autonomous way (without human intervention)

## Slide 7: Non functional req
Countries where the system will be sold: Europe, USA, ..
  Will induce choices on power supply, like 110V 220V, 50 60hz, plugs and cords
  Will induce constraints on certifications, like CE label, ..
Usability
  Any non technical person should be able to use the system without training
Efficiency
  power consumption less than 40w
Min surface of house that can be cleaned with no interruption = 100sqm
  Will induce NF req on capacity of battery, power of engines etc
  Will induce NF req on consumption of ‘software’
Safety: no harm to people, animals, objects
  Speed of robot no more than .. m/sec

## Slide 8: Domain requirements
(hidden requirements about the domain)
  Floor of house is flat
  Floor of house is mildly dirty (no heavy dirt like in industrial environment)
  No liquids on floor

## Slide 9
Note about NFR: these NFR are system level, so do not follow the taxonomy of sw requirements (ISO 9126, maintainability portability efficiency …)
Note about FR: the system is actually just an aggregate of robot, charging station, mobile app, most of the FR are allocated to robot and mobile app. In the following FRs are grouped per robot and mobile app

## Slide 10: F requirements (Robot level)
Monitor safety
  Monitor speed and limit it to .. m/sec
  Stop if obstacle encountered
  Force shutdown in case of harmful situation
Manage Energy
  Read battery capacity
  Estimate distance that can be travelled with current capacity
  Monitor recharge of battery
Manage upgrades
  Check if upgrade is available
  Read current version number
  Download firmware upgrade
  Install firmware upgrade
Self test
  Check each component (sensors, engines, ..) a, b .. and notify defects in case of.
Manage remote communications
  Send / receive messages with company server

## Slide 11: F requirements (Robot level)
Manage movement of robot
  Move from position A (here) to position B
  Define a turnaround of an obstacle
  Define a turnaround of a gap
  Cover (and clean) a surface
    Define a path to cover all the surface
    Follow a given path
  Learn a house map of the surface of the house
  Interrupt / resume a surface cover
Manage Obstacle
  Recognize obstacle (fixed, movable, moving)
  Recognize gap
Clean
  Operate cleaning device
  Check if floor is clean (feasible??)

## Slide 12: F requirement (smartphone level)
Manage user interaction (on smartphone app)
  Set robot On off
  Start
  Learn
  Show history (when cleaned, how long)
  Show consumption
  Show path followed for cleaning
  Show map and obstacles
  Modify map
  Define plan of cleanings for week / day / month

## Slide 13: UCD

## Slide 14: UC1 - clean
Precondition
  Robot is ON
  Robot is in charging station
Post condition
  Robot is in charging station
Scenarios
  UC1.1 Nominal: map is available, robot fully cleans the house, no unknown obstacles encountered
  UC1.2 Exception: map is not available, no cleaning
  UC1.3 Variant: map is available, battery not enough, robot cleans partially then returns for charging, then recovers cleaning
  UC1.4 Variant: map is available, robot fully cleans the house, unknown obstacle is encountered and bypassed
  UC1.5 Exception: map is available, unknown obstacle is encountered and cannot be bypassed, robot stops 10 seconds then returns to charging station, house partially uncleaned
  UC1.6 Exception: map is available, self test not passed, robot remains at charging station

## Slide 15: Map of house
A1 (charging station) | A2 | A3
B1 | B2 | B3
C1 | C2 | C3

## Slide 16: UC1.1
Precondition
  Robot is ON
  Robot is in charging station
  Battery is charged
  Map of house is available (2d model made of tiles, tiles tagged as free/obstacle/gap)
Postcondition
  Robot has cleaned the house (all tiles of house have been covered by robot path)
  Robot is in charging station

## Slide 17: UC1.1
Robot computes path to clean house, using available map (path = A1, A2, A3, B3, B2, B1, C1,C2,C3, B3 A3 A2 A1…)
Robot moves to A2 and cleans
Robot moves to A3 and cleans
……
Robot moves to A1 and stops

## Slide 18: UC1.2
Precondition
  Robot is ON
  Robot is in charging station
  Battery is charged
  Map of house is not available
Postcondition
  Robot has not cleaned the house
  Robot is in charging station

## Slide 19: UC1.2
Robot tries to compute path, map is not available
Robot does not move

## Slide 20: UC1.3
Precondition
  Robot is ON
  Robot is in charging station
  Battery is partially charged
  Map of house is available (2d model made of tiles, tiles tagged as free/obstacle/gap)
Postcondition
  Robot has cleaned the house (all tiles of house have been covered by robot path)
  Robot is in charging station

## Slide 21: UC1.3
Robot computes path to clean house, using available map (path = A1, A2, A3, B3, B2, B1, C1,C2,C3, B3 A3 A2 A1… assuming house is squared, 9 tiles, charging station in A1)
Robot moves to A2 and cleans
Robot moves to A3 and cleans
Robot recognizes battery level low
Robot computes path from A3 to A1 (A3, A2, A1)
Robot moves to A2
Robot moves to A1
Robot waits for battery charged
Robot computes path to A3 (where interrupted) (A1, A2, A3)
Robot moves to A2
Robot moves to A3
(recover cleaning) robot moves to B3 and cleans
(from now same as UC1.1)

## Slide 22: UC1.4
Precondition
  Robot is ON
  Robot is in charging station
  Battery is charged
  Map of house is available (2d model made of tiles, tiles tagged as free/obstacle/gap)
Postcondition
  Robot has cleaned the house (all tiles of house have been covered by robot path)
  Robot is in charging station

## Slide 23: UC1.4
Robot computes path to clean house (using UC manage movement), using available map (path = A1, A2, A3, B3, B2, B1, C1,C2,C3, B3 A3 A2 A1… assuming house is squared, 9 tiles, charging station in A1)
Robot moves to A2 (using UC manage movement) and cleans
Robot moves to A3 and cleans
Robot tries to reach B3 but finds obstacle (using UC manage obstacle)
Robot computes path to B2 avoiding B3 (A3, A2, B2) (using UC manage movement)
Robot moves to A2
Robot moves to B2 and cleans
From now on same as UC1.1

## Slide 24: UC2 Manage upgrades
Precondition
  Robot is on
Scenarios
  UC2.1 Nominal: check for upgrades on maintenance server, one is available, download, upgrade is ok, install
  UC2.2 Variant: check for upgrades, none is available
  UC2.3 Variant: check for upgrades, one is available, download, upgrade is corrupted, repeat download, upgrade is ok, install
  UC2.4 Exception: check for upgrades, communication down, abort

## Slide 25: Glossary

## Slide 26: System design

## Slide 27: Deployment diagram

## Slide 28
In the following each component of the system (robot, charging station, smartphone app) should be analysed producing a possibly complete requirement document
  Robot
    Context diagram, interfaces
    FR, NFR
    UCD
    System design
    Deployment diagram (not needed in this case)
  Smartphone app
    Context diagram, interfaces
    FR, NFR
    UCD
    System design (not needed in this case)
    Deployment diagram (not needed in this case)

## Slide 29: Robot
Context diagram
  User
  Charging station
  Obstacles
  Maintenance server of company
FR
  See slides 10, 11
  Send / receive messages with smartphone app