## Slide 1: RVC
Robot Vacuum Cleaner

## Slide 2: RVC system
System point of view
As if we were a company producing the RVC system
Dyson, Ariete, Moulinex

## Slide 3: Req document
Stakeholders
Context diagram + interfaces
FR + NFR
UCD + UC + scenarios
Glossary
System design
Deployment diagram

## Slide 4: Stakeholders
End users (customers who will use the RVC system)
Component producers
Retailers (mediaworld ..)
Competitors
Std for power supply
Environment (houses or offices or industrial?)
Inside company
  Marketing office
  Design office
  Software office
  Engineering office

## Slide 5: Context diagram
Actor: end user
Actor: power supply
Actor: maintenance server
interfaces
Actor | Log interface | Physical interface
End user | Start stop , .. | 3 buttons
Power supply |  | Plug schuko 3 poles, 220v
Maintenance server of producer company | Look for update, install update | Wifi connection

## Slide 6: Functional requirement (system level)
Clean floors of house in autonomous way (without human intervention)

## Slide 7: Non functional req
Countries where the system will be sold: Europe, USA, ..
  Will induce choices on power supply, like 110V 220V, 50 60hz, plugs and cords
  Will induce constraints on certifications, like CE label, ..
Usability
  Any non technical person should be able to use the system without training
Efficiency
  power consumption less than 40w
Min surface of house that can be cleaned with no interruption = 100sqm
  Will induce NF req on capacity of battery, power of engines etc
  Will induce NF req on consumption of ‘software’
Safety: no harm to people, animals, objects
  Speed of robot no more than .. m/sec

## Slide 8: Domain requirements
(hidden requirements about the domain)
  Floor of house is flat
  Floor of house is mildly dirty (no heavy dirt like in industrial environment)

## Slide 9
Note about NFR: these NFR are system level, so do not follow the taxonomy of sw requirements (ISO 9126, maintainability portability efficiency …)

## Slide 10: F requirements (Robot level)
Safety requirements
  Monitor speed and limit it to .. m/sec
  Stop if obstacle encountered
  Force shutdown in case of harmful situation
Manage Energy
  Read battery capacity
  Estimate distance that can be travelled with current capacity
  Monitor recharge of battery
Manage upgrades
  Check if upgrade is available
  Read current version number
  Download firmware upgrade
  Install firmware upgrade
Self test
  Check each component (sensors, engines, ..) a, b .. and notify defects in case of
Manage remote communications
  Send / receive messages with company server

## Slide 11: F requirement (Robot level)
Manage movement of robot
  Move from position A (here) to position B
  Define a turnaround of an obstacle
  Define a turnaround of a gap
  Cover (and clean) a surface
    Define a path to cover all the surface
    Follow a given path
  Learn a house map of the surface of the house
  Interrupt / resume a surface cover
Manage Obstacle
  Recognize obstacle (fixed, movable, moving)
  Recognize gap
Clean
  Operate cleaning device
  Check if floor is clean (feasible??)

## Slide 12: F requirement (smartphone level)
Manage user interaction (on smartphone app)
  Set robot On off
  Start
  Learn
  Show history (when cleaned)
  Show consumption
  Show path followed for cleaning
  Show map and obstacles
  Modify map
  Define plan of cleanings for week / day / month

## Slide 13: UC, scenarios

## Slide 14: Glossary

## Slide 15: System design

## Slide 16: Deployment diagram

## Slide 17
In the following each component of the system (robot, charging station, smartphone app) should be analysed producing a possibly complete requirement document
  Robot
    Context diagram, interfaces
    FR, NFR
    UCD
    System design
    Deployment diagram (not needed in this case)
  Smartphone app
    Context diagram, interfaces
    FR, NFR
    UCD
    System design (not needed in this case)
    Deployment diagram (not needed in this case)

## Slide 18: Robot
Context diagram
  User
  Charging station
  Obstacles
  Maintenance server of company
FR
  See slides 10, 11
  Send / receive messages with smartphone app